## Slide 1: Data quality & VGI Ordnance Survey GB
COST Action TD1202 Final Meeting, RGS, London, 13/10/16
Jeremy Morley
Jenny Harding & Claire Pook
April 2017

## Slide 2: Outline
Context - Data quality and Ordnance Survey workflow
VGI and quality in current products and applications
Research – applying VGI approaches

## Slide 3: Data Quality management aims
Consistent and sustainable quality
Customer requirement
Risk management
ISO 19158 Geographic Information:
Quality Assurance for data supply

## Slide 4: traditional data set-ups are being challenged
BI & analytics
Data warehouse
Spatial Database
Mapping and ETL
Dashboards
Reporting
Staging
Data collection and
Source Systems
OLTP
ERP
CRM
LOB
Data Access/Services
POI
Map
Navigation
Image

## Slide 5: Digitisation produces data volume and silos
Increasing data volumes
1
50x Data growth 2010-2020
40ZB Digital Universe 2020
1Trillion Web pages
BI & analytics
Data warehouse
Spatial Database
Mapping and ETL
Dashboards
Reporting
Staging
Data collection and
Source Systems
OLTP
ERP
CRM
LOB
Data Access/Services
POI
Map
Navigation
Image

## Slide 6: real time response and action is required
Dashboards
Reporting
BI & analytics
Data warehouse
Spatial Database
Mapping and ETL
Dashboards
Reporting
Staging
Data collection and
Source Systems
OLTP
ERP
CRM
LOB
Data Access/Services
POI
Map
Navigation
Image
Real-Time Data/Response
2
Increasing data volumes
1

## Slide 7: Less than 20% of iot data is structured
Navigation
Real-Time
2
New data
Devices
Web
Sensors
Social
New data types
15x
Machine generated data 2020
1.3M Hours on Skype per hour
2.4M
Facebook content per minute
Dashboards
Reporting
BI & analytics
Data warehouse
Spatial Database
Mapping and ETL
Dashboards
Reporting
Staging
Data collection and
Source Systems
OLTP
ERP
CRM
LOB
Data Access
POI
Map
Image
Increasing data volumes
1
3

## Slide 8: Data lives and breathes in the cloud
Real-Time
2
New data
Devices
Web
Sensors
Social
New data types
Dashboards
Reporting
BI & analytics
Data warehouse
Spatial Database
Mapping and ETL
Dashboards
Reporting
Staging
Data collection and
Source Systems
OLTP
ERP
CRM
LOB
Data Access
Increasing data volumes
1
3
4
Cloud-born data
$100B spend on cloud
50% large orgs have hybrid by 2017
40% CRM sold are SaaS

## Slide 9: where in the workflow DOES VGI FIT?
Change detection
Production area
Production area
Production area
VGI
Database
Products & services
Products & services
Products & services
Products & services
QC
customers
Specification of data & accreditation of suppliers
Quality Assurance – analysis & investigation
Quality management information
VGI (?)
Notes: Supplier accreditation to ISO 19158 standard

## Slide 10: VGI CONTINUUM
Passive data mining
Crowd defines and owns the problem
Crowd uploaders
Crowd sensors
Crowd contributors
Crowd visual processors
Crowd scientists / analysts / engineers

## Slide 11: VGI – ELEMENTS of SUCCESS
ADVERTISING Do people hear about the project?
MOTIVATION Are they interested in the proposition?
HUMAN FACTORS Is the system usable, maybe even fun?
Notes: Motivation – singular proposition (tell us vernacular geography names by postcode) vs multi-purpose (OSM – many reasons to engage)
System - may be considering HCI of a web interface; but the system in OSM is much broader

## Slide 12: COVERAGE OF Our Current PhDs
Crowd-sourcing & land rights in crofting communities Edinburgh
GeoBIM Newcastle
Negotiating Environments - tracking environmental and mediated information use Swansea
Enriching 3D Building Models Cardiff
Situational Relevance of Mobile Maps and Media Nottingham
Geo-spatial Technology and Sensory Geographies Royal Holloway
3D data requirements & quality UCL
Temporal activity modelling of cartographic objects Southampton
Exploiting multiray photogram. for urban 3D Newcastle
Deep Learning Lancaster
Vernacular geography & personal data Nottingham Horizon CDT
Automated map content selection for multi-modal travel Edinburgh
Detecting Transient Geographies Southampton Web Sciences
Realtime Urban Data Spaces UCL CASA
Mapping Vernacular Geographies in Places of Super-Diversity Royal Holloway
Role & uses of location & vernacular geography within identities of people and communities Nottingham
3D
Analytics
Design for human use
Places & spaces
Natural Language - spatial location descriptions Massey (NZ)
Human-Machine Interfaces for navigation of autonomous vehicles Nottingham
Machine learning to derive vernacular geography from social media RHUL
Geography of events from social media Swansea + SME (Blurrt)
Notes: Further details of running PhD projects can be provided as slide decks or posters from our February research days

## Slide 13: COVERAGE OF Our Current PhDs
Crowd-sourcing & land rights in crofting communities Edinburgh
Enriching 3D Building Models Cardiff
Vernacular geography & personal data Nottingham Horizon CDT
Detecting Transient Geographies Southampton Web Sciences
Role & uses of location & vernacular geography within identities of people and communities Nottingham
3D
Analytics
Places & spaces
Machine learning to derive vernacular geography from social media RHUL
Geography of events from social media Swansea + SME (Blurrt)
Notes: Further details of running PhD projects can be provided as slide decks or posters from our February research days

## Slide 14: OS Maps – contributed routes
Routes shared in OS Maps app
500 000+ routes submitted for shared use
Mix of traced routes and uploaded GPS tracks
Notes: Data content not used by os – is for users to share
But if were to…
Quality:
Posiitonal:
Digitsed can have few points, long straight sections between them eg sometimes cutting through buildings
Uploaded gps tracks can have odd spikes – possibly where GPS signal lost
Coverage: some areas low density – why? Even when there are public footpaths present
Uses??

## Slide 15: Tell OS – reporting of errors/omissions
Tool: A web map interface to enable reporting of errors/omissions
Open to public sector users
Good use levels –
c200 reports/month
Process:
Select product
Find location
Submit data……
Notes: Can also report to CSC via email

## Slide 16: TELL OS
Contribution acknowledged +action taken
Data stored and feeds into job operations planning
Reported points viewable by users
Notes: Drop down list of response types
Trusted users – spelling changes accepted – edit made by OS QA there and then
New building – QA check against imagery – create job for field or photogrammetric capture

## Slide 17: MCA ‘Fintan’ – expert VGI on local names
Web map service application for coastguard knowledge of local names
Users: operators in centralised control room for search and rescue services
Also includes names contributed by volunteer Coastguard Officers
Database contains around 6100 names with point, line or polygon location geometry
Notes: In Irish mythology – the Salmon of Knowledge
Maps – can zoom to OSMM. Contains os gazetteer data
Quality: VG so enables capture of alternative spellings
Positional? Completeness? - any info better than none?
Attributes consistency– use of codes eg for buoys, stretches of rivers – but free text (?)

## Slide 18: Crowd-sourcing & land rights in crofting communities Edinburgh
Courtesy of Rica DUCHATEAU William MACKANESS Edinburgh Uni
Notes: PhD Exploring efficacy of crowd sourcing for recording boundary and land rights information
Focused on Scotland (Highlands and Islands) crofting community – form of land tenure and small scale food production (less than 50ha)
Current Registers of Scotland Crofting Register relies of crowdsourcing through hand drawn maps- RoS then digitise on OSMM.
In 2012 , still c 15000 not yet digitally spatially referenced.
(Used for croft registration applications and resolving boundary disputes)
Croftcapture app for smartphone use in field, based on OS OpenSpace SDK – software development kit
Blue line = boundary captured using app
Red line= boundary digitised from osmm
Potential benefit of app – submit already digitised using OS Open data
Crofters in sample area invited to participate
Positional accuracy errors of up to 7m in small sample – too much for land administration uses?
App developed in MSc.
PhD Focused on socio-technical issues of:
Community capacity to record and validate such info
Delineation of boundaries without physical features
Robustness of data to legal scrutiny

## Slide 19: Zooniverse project

## Slide 20: Applications chosen for trial
Street furniture
Business names
Notes: But for now, the application that I’ve chosen to develop will allow users to tag street furniture and business names in stereo pairs of mobile mapping imagery.
Using photogrammetry software, I can then generate a 3D real world coordinate for each feature.
This could potentially feed in to a Utilities layer in our data, or contribute to the data capture required for the smart cities project.
Everybody knows what a lamp post looks like, and this application lets you go on a tour of the city where the imagery was taken.
You don’t need to have specialised point cloud software installed (it’s just a web browser), don’t need the ability to work with point clouds…

## Slide 21: Available Ground-Based Imagery
Notes: The mobile mapping imagery we currently have available in BC&I is of Bournemouth.
It was captured last Summer using a Leica Pegasus 2, a vehicle mounted laser scanner that also has 7 georeferenced cameras on board.
Here’s the route that was taken, and the orientation of the cameras based on the forward direction of travel.

## Slide 22: How it works
Notes: This is a stereo pair of images, and all the user has to do is identify whether there’s a lamp post that can be clearly seen in both images, and then click at the base.
We are looking at how this will work with just one image, but at the moment you have to look for the matching feature, and identify it in both images..

## Slide 23: How it works

## Slide 24: How it works
Notes: Draw a polygon around the business name you’ve spotted, and choose the business type from a drop down list.
We don’t yet have the functionality to actually type what you see, but that’s something that will be available in the future..

## Slide 25: How it works

## Slide 26: Processing the data
Left hand image coordinates (Xlocal, Ylocal)
Exterior orientation of both cameras (OSGB36 & omega, phi, kappa)
Real world coordinates of lamp post (OSGB36)
Right hand image coordinates (Xlocal, Ylocal)
Notes: So here’s how I’ll take all the clicks and turn them into real world OSGB coordinates using the principles of aerial triangulation…

## Slide 27: Results (IDEAL!)
Notes: Here’s an image showing what our results might look like if we had imagery of our local area here.
There will be small clusters of coordinates all representing the same feature, so I’ll take the average of these to choose the best position. That the advantage of having numerous people view the imagery and tag the features.
Also with the business name application, I’ll be able to extract the defined polygon from the imagery, creating nice visual of what it was the user saw in the original imagery. These may also become candidates for further crowdsourced transcription tasks. Or maybe we could look at Optical Character Recognition to read what they say automatically.

## Slide 28: pilot
18 volunteers asked to take part, contributing as often as they were able
Over 5000 classifications achieved in 6 weeks
Chart: Contributions per user
| tappleton | mfarthing | stefantaylor | deadmanmoz | rich_milner | Rbushaway | JuliaMatheson | ajgardi | jbraybrook | razzder | skatebirder | bruszi | jhos | RolloHome | Ngoodwyn | cchambers83 | animationtrev | natalieridal
 | 2128 | 1057 | 769 | 282 | 190 | 156 | 87 | 86 | 66 | 62 | 51 | 44 | 40 | 25 | 16 | 6 | 2 | 1
Notes: Each user had a log in, meaning I could track contributions to their owner
Instructions vs ‘having a go’
Feedback at he end of the pilot

## Slide 29: Pilot results (Lamp posts)

## Slide 30: Pilot results (Business Names)

## Slide 31: Zooniverse Project - Some Things to consider
We do not hold a national dataset of mobile-mapping imagery yet(!)
Information is only as current as the last time the photos were taken
Objects may be obscured by vehicles/people/trees etc
WHAT’s NEXT?
How can staff be encouraged to contribute?
Future research into crowd sourcing in a commercial environment
Notes: We do not hold a national dataset of mobile-mapping imagery yet(!)
Information is only as current as the last time the photos were taken
Objects may be obscured by vehicles/people/trees etc
How could OS staff be encouraged to contribute in their spare time?
Future research into crowd sourcing in a commercial environment

## Slide 32: VGI research – SOME QUESTIONS (1)
How do many contributors do we need?
1,000,000 people to contribute 3 times each; or
1,000 people to contribute 3,000 time each?
Long-tail distribution?
Advertising x Motivation x Retention rate (human factors / task design)
Do contributors produce better results with longer retention (more training)? Or do they get over-trained?
Do social functions help, such as chat rooms – community aspects, unexpected discoveries?
Can we convert from ”tasked contributors” to crowd-defined requirements?

## Slide 33: VGI research – SOME QUESTIONS (2)
How to assess quality of VGI in ways that minimise manual checks?
How to design task flow and interfaces to help ensure quality of input?
How to present meaningful information about quality to data users?
How to maintain engagement and motivation of contributors?

## Slide 34
Jeremy Morley, Jenny Harding & Claire Pook
jeremy.morley@os.uk jenny.harding@os.uk, claire.pook@os.uk
023 8005 5764